| Definitions Construction Product: A product or ‘kit’ which is produced and placed on the market for permanent incorporation in construction works, and whose performance influences at least one of the basic requirements for works. (The Interpretative Documents to the CPD (also relevant to the CPR) describe “permanent incorporation” as meaning the products removal reduces the performance capabilities of the works and/or the dismantling or replacement of the product involves construction activity.) Kit: A construction product placed on the market as a set comprising at least two separate components which need to be put together so that the kit can be incorporated into the construction works. Construction Works: A building or civil engineering construction. Basic Requirements for Construction Works: A set of requirements that a construction works must satisfy over an economically reasonable working life, subject to normal maintenance being undertaken. Harmonised Technical Specification: This can take two forms: - A harmonised European Standard (hEN) A European Assessment Document (EAD) Both will give information on the regulated characteristics that a product must satisfy to enable CE marking to take place. | Steps to deciding if a product must carry CE marking Step Action Step1 Decide if product is a construction product as defined under the CPR. See definition of what a construction product is. Step 2 Check if a Harmonised Technical Specification exists for the product. Follow the link below to the Europa website to check if a Harmonised European Standard (hEN) exists: https://ec.europa.eu/growth/single-market/european-standards/harmonised-standards/construction-products_en If a hEN exists, then the product needs to carry the CE marking. If no hEN exists, check if a European Technical Approval Guideline (ETAG) exists under the CPD or a European Assessment Document (EAD) exists under the CPR. Follow the link below: - https://www.eota.eu/en-GB/content/etags-used-as-ead/26/ (for ETAGs) https://www.eota.eu/en-GB/content/eads/56/ (for EADs) An ETAG or EAD arises from a mandate issued by the European Commission and EFTA. This means that other manufacturers have made application for an ETA [European Technical Approval (CPD) or European Technical Assessment (CPR)] and have the same or similar product on the market which carries the CE marking. Companies now have to decide whether or not to apply for an ETA enabling them to apply their CE marking. If a product falls within the scope of an EAD, it remains a voluntary decision for the manufacturer whether or not to request an ETA for it and to that extent, CE marking will remain voluntary for such products. Step 3 If the product is not covered by a hEN or an ETA. No CE marking under the CPR is possible. |
| --- | --- |